## Slide 1
LINC-NIRVANA on its way to the sky

## Slide 2
What is LINC-NIRVANA
High Resolution, NIR Imager:
MCAO, Interferometry
λ: JHK
Platescale: 5.11 mas/px
Resolution: 10 mas (J)
15 mas (H)
20 mas (K)
FoV: 10.5 x 10.5 arcsec

## Slide 3
Wide FoV for low layers
Narrow FoV for high layers

## Slide 4
Delay line/Piston mirror
Visible/NIR dichroic
Science channel cryostat
High layer Wavefront Sensor
K-mirror
6 arcmin FoV
Annular Mirror
Ground layer Wavefront Sensor
Deformable mirror

## Slide 6
Build
Implement
Science
Build
Implement
Science
Build
Implement
Science
Build
Implement
Science
Resources
Time
LINC/SCAO (on-axis, self referencing interferometry)
GLAO
MCAO
NIRVANA
(MCAO-fed, off-axis interferometry)
Yaaaawn….too easy!
Mmmm…I knew it was going to end like this…
LINC-NIRVANA original plan

## Slide 7
Build
Implement
Science
Build
Implement
Science
Build
Implement
Science
Build
Implement
Science
Resources
Time
LINC/SCAO (on-axis, self referencing interferometry)
GLAO
MCAO
NIRVANA
(MCAO-fed, off-axis interferometry)
Yaaaawn….too easy!
Mmmm…I knew it was going to end like this…
Pathfinder
LINC-NIRVANA original plan

## Slide 8
Item | Value / Comment
Mode | Multi-Conjugate Adaptive Optics Near-IR imaging
Wavelength | 1.1 – 2.4 µm; broad and narrow band filters
Plate Scale | 5.11 mas per pixel
Spatial Resolution | 30 mas – J Band 41 mas – H Band (FWHM of diffraction-limited peak) 53 mas – K Band
Field of View | 10.5” (110 square arcsec)
Adaptive Optics | 2-layer, multi-conjugate with 12 NGS for GLAO and 8 NGS for high-layer AO. The deformable mirrors have 672 (ground) and 349 (high) actuators
Strehl Ratio | J-band 20% H-band 40% (based on simulations) K-band 60%
Sky coverage | Galactic plane 99% North Galactic Pole 48%
Lean MCAO

## Slide 9
After commissioning LINC-NIRVANA will support:
    «campaign mode» JHK interferometry.
    Natural guide stars MCAO in a 10 x 10 arcsec FoV.
What we want:
    Largest possible FoV (41 or 82 arcsec).
Proposed Upgrade

## Slide 10
Gemini -GeMS First Light
10.5”
41”
Now
41” Upgrade
Courtesy of Tom Herbst

## Slide 11
82”
41” Upgrade
82” Upgrade
Courtesy of Tom Herbst

## Slide 12: Preliminary Work…
(D. Greggio & P. Bizenberger)
All designs:
  Are diffraction limited 1 – 2.5 μm.
  Cost ca. 500 k€.
  Fit within existing cryostat.

## Slide 13
Item | Value / Comment
Mode | Multi-Conjugate Adaptive Optics Near-IR imaging
Wavelength | 1.1 – 2.4 µm; broad and narrow band filters
Plate Scale | 5.11 mas per pixel (20 mas/pixel)
Spatial Resolution | 30 mas – J Band 41 mas – H Band (FWHM of diffraction-limited peak) 53 mas – K Band
Field of View | 10.5” (110 square arcsec) (Wide field optics give 41’’ square with a 2k detector and 82’’ square with a 82’’ detector).
Adaptive Optics | 2-layer, multi-conjugate with 12 NGS for GLAO and 8 NGS for high-layer AO. The deformable mirrors have 672 (ground) and 349 (high) actuators
Strehl Ratio | J-band 20% H-band 40% (based on simulations) K-band 60%
Sky coverage | Galactic plane 99% North Galactic Pole 48%
Lean MCAO
Upgrade

## Slide 14
Residual WF RMS Error (nm)
Time (s)
50
100
150
200
250
300
350
400
450
0
5
10
15
20
25

## Slide 15
Departure | Arrival | Mode of transport | Distance [km] | Time [d]
MPIA | Neckarsteinach | Lowboy Trailer | 18 | <1
Neckarsteinach | Bremerhaven | Riverboat | 700 | 7
Bremerhaven | Los Angeles | Cargo ship | 15120 | 23
Los Angeles | LBT basecamp | Lowboy Trailer | 970 | 2
LBT basecamp | LBT summit | Lowboy Trailer | 45 | <1
TOTAL |  |  | 16850 | 50

## Slide 17
Departure | Arrival | Mode of transport | Distance [km] | Time [d]
MPIA | Neckarsteinach | Lowboy Trailer | 18 | <1
Neckarsteinach | Bremerhaven | Riverboat | 700 | 7
Bremerhaven | Los Angeles | Cargo ship | 15120 | 23
Los Angeles | LBT basecamp | Lowboy Trailer | 970 | 2
LBT basecamp | LBT summit | Lowboy Trailer | 45 | <1
TOTAL |  |  | 16850 | 50

## Slide 18
Run | Period | Comments
I1 | 11 – 17 June 2015 | Dismantiling of Pathfinder
I2 | 09 – 25 November 2015 | Receipt & bench installation
I3 | 12 – 28 January 2016 | GWSs internal alignment
I4 | 23 – 04 Feb/March 2016 | Bench & cryostat integration
I5 | 01 – 16 March 2016 | Warm Optics alignment (both sides)
I6 | 12 – 26 April 2016 | HWSs internal alignment & loop
I7 | 04 – 11 May 2016 | Annular mirrors alignment
I8 | 26 – 09 May/June 2016 | Close loop with WFSs in lab
I9 | 10 – 21 June 2016 | Cryostat + Instrument verification
I10 | 20 – 02 Sept/Oct 2016 | Installation at instrument platform
LINC-NIRVANA re-integration plan
We are here

## Slide 20
What next?
Conclude internal re-alignment of the instrument.
Align LINC-NIRVANA to the telescope.
Commissioning.
Camera upgrade?
Interferometry?